## Slide 1: A Manual for Restart of ECHO2D and Arbitrary Bunch Shape
Igor Zagorodnov
1 April 2020

## Slide 2: Contents
New Parameters.
Restart procedure.
Example of TESLA cavity.
First half of the cavity.
Restart and the second half of the cavity.
Comparison
Wake monitor

## Slide 3: 1. New parameters.
StartPosition =n
Parameter n defines an initial z-position of the moving mesh.
The mesh head is placed at position n*StepZ.
InFieldDir=string/-
This parameter defines the directory with initial fields.
DumpField=0/1
This parameter defines whether the final field will be dumped (1) or not (0).

## Slide 4: 2. Restart procedure.
Let us suggest that in the first step we have done TimeSteps=N1 time steps from StartPosition=0. The parameter DumpField has to be 1. The dumped fields are in files “Field_m.bin” in directory “round”.
Before to restart you should create directory “InField” and place the dumped filed files “Field_m.bin” there. Other parameters should be:
StartPosition=N1 (N1 from first run)
TimeSteps= N2 (a desired number of time steps in the second run)
InFieldDir=InField (take initial fields of the first run)
In the next slides an example is considered.

## Slide 5: 3. Example of TESLA cavity.
%%%%%%%%%%%%%% geometry
GeometryFile=tesla9.txt % -(Gaussian beam)
Units=cm % -m/cm/mm
GeometryType=round' % recta / round
Width=0 % in meters
SymmetryCondition=magn % magn/elec
Convex=1
%%%%%%%%%%%%%% beam and field
InPartFile=-
BunchSigma=0.005
Offset=5
InFieldDir= -
%%%%%%%%%%%%%% model
WakeIntMethod=ind
Modes=1 0
%%%%%%%%%%%%%% mesh
MeshLength=52
StepY=0.001
StepZ=0.001
NStepsInConductive=0
StartPosition=0
TimeSteps=1116
%%%%%%%%%%%%%% monitors
DumpField=0

## Slide 6: 3. Example of TESLA cavity.
The calculation is done for monopole and dipole mode up to the end of the cavity with indirect integration at the end.
The initial fields are calculated in the program as field in the ingoing pipe.

## Slide 7: 3. Example of TESLA cavity.
Loss=5.198 V/pC
Kick=38.984 V/pC/m

## Slide 8: 4. First half of the cavity.
%%%%%%%%%%%%%% geometry
GeometryFile=tesla9.txt % -(Gaussian beam)
Units=cm % -m/cm/mm
GeometryType=round' % recta / round
Width=0 % in meters
SymmetryCondition=magn % magn/elec
Convex=1
%%%%%%%%%%%%%% beam and field
InPartFile=-
BunchSigma=0.005
Offset=5
InFieldDir= -
%%%%%%%%%%%%%% model
WakeIntMethod=dir
Modes=1 0
%%%%%%%%%%%%%% mesh
MeshLength=52
StepY=0.001
StepZ=0.001
NStepsInConductive=0
StartPosition=0
TimeSteps=500
%%%%%%%%%%%%%% monitors
DumpField=1

## Slide 9: 4. First half of the cavity.
The calculation is done for monopole and dipole mode along 500 mm with direct integration.
The initial fields are calculated in the program as fields in the ingoing pipe.
The final fields are dumped in directory “round”.

## Slide 10: 3. First half of the cavity.
Loss1=2.197 V/pC
Kick1= 19.142 V/pC/m

## Slide 11: 5. Second half of the cavity.
%%%%%%%%%%%%%% geometry
GeometryFile=tesla9.txt % -(Gaussian beam)
Units=cm % -m/cm/mm
GeometryType=round' % recta / round
Width=0 % in meters
SymmetryCondition=magn % magn/elec
Convex=1
%%%%%%%%%%%%%% beam and field
InPartFile=-
BunchSigma=0.005
Offset=5
InFieldDir= InField
%%%%%%%%%%%%%% model
WakeIntMethod=ind
Modes=1 0
%%%%%%%%%%%%%% mesh
MeshLength=52
StepY=0.001
StepZ=0.001
NStepsInConductive=0
StartPosition=500
TimeSteps=616
%%%%%%%%%%%%%% monitors
DumpField=1

## Slide 12: 5. Second half of the cavity.
The fields from the previous run are copied todirectory “InField”.
The calculation is done for monopole and dipole mode along 616 mm with indirect integration in the outgoing pipe.
The initial fields are taken from directory “InField”.
The final fields are dumped in directory “round”.

## Slide 13: 5. Second half of the cavity.
Loss2= 2.996 V/pC
Kick2= 19.807 V/pC/m

## Slide 14: 6. Comparison.
Loss1+Loss2= 5.20 V/pC
Loss=5.20 V/pC
Kick=38.98 V/pC/m
Kick1+Kick2=38.95 V/pC/m

## Slide 15: 7. Wake monitor.
The input.txt file has a new parameter
"WakeMonitor=nt0 nt1 ngap",
where
nt0 -first time step for wake to be saved;
nt1 -last time step for wake to be saved;
ngap - gap between the savings.
The wakes are saved in binary files with names "wakeM_m_nt.bin",
Where
m - mode number;
nt -time step number.
The binary format is simple and can be understood if you take a look in Matlab script "A_WakeMonitor.m".

## Slide 16: 8. Arbitrary bunch shape.
The current profile is generated in ECHO from arbitrary 1D particle distribution. I have decided to use this option as later it will allow an arbitrary 3D bunch shape.
Here a short instruction.
1. In order to prepare an arbitrary shape use a modification of "ParticleGenerator_Triangular_1D.m" . It generates 1D particle distribution.
This file prepares a triangular shape. In order to have an arbitrary shape modify the form factor function at the beginning of the file.
The generated particle file "particles.in" has the format:
N, x1,x2,...,xN,
where N is the number of particles and xi is the longitudinal coordinate in the bunch frame.
2. In file "input_in.txt" the name of the particle file should be written "InPartFile=particles.in."
For the default Gaussian bunch use as before "InPartFile= - ".
3. Start now ECHO_GUI.exe and run it with " tesla9.echo2d ". You should see a triangular shape of bunch.
4. To analyze the wake run " PP_Wake_Monopole_AnyShape.m ". I have not prepared a dipole script but you can easily to make it from "PP_Wake_Dipole.m ".
5. The wake coordinates in "WakeL_00.txt" start now at 0. In the previous version the start position was "-5*sigma". Due to this change some of old matlab scripts could have problems.
6. The 1D bunch shape interpolated from particles and indeed used in ECHO is saved in "current0.txt". It is approximately the form factor function.