## Slide 1: A Manual for Wake Monitor and Arbitrary Bunch Shape
Igor Zagorodnov
1 April 2020

## Slide 2: Contents
Wake monitor
Arbitrary bunch shape

## Slide 3: 3. Example of TESLA cavity.

## Slide 4: 1. Wake monitor.
The input.txt file has a new parameter
"WakeMonitor=nt0 nt1 ngap",
where
nt0 -first time step for wake to be saved;
nt1 -last time step for wake to be saved;
ngap - gap between the savings.
The wakes are saved in binary files with names "wakeM_m_nt.bin",
Where
m - mode number;
nt -time step number.
The binary format is simple and can be understood if you take a look in Matlab script "WakeMonitor.m".

## Slide 5: 2. Arbitrary bunch shape.
The current profile is generated in ECHO from arbitrary 1D particle distribution. I have decided to use this option as later it will allow an arbitrary 3D bunch shape.
Here a short instruction.
1. In order to prepare an arbitrary shape use a modification of "ParticleGenerator_Triangular_1D.m" . It generates 1D particle distribution.
This file prepares a triangular shape. In order to have an arbitrary shape modify the form factor function at the beginning of the file.
The generated particle file "particles.in" has the format:
N, x1,x2,...,xN,
where N is the number of particles and xi is the longitudinal coordinate in the bunch frame.
2. In file "input_in.txt" the name of the particle file should be written "InPartFile=particles.in."
For the default Gaussian bunch use as before "InPartFile= - ".
3. Start now ECHO_GUI.exe and run it with " tesla9.echo2d ". You should see a triangular shape of bunch.
4. To analyze the wake run " PP_Wake_Monopole_AnyShape.m ". I have not prepared a dipole script but you can easily to make it from "PP_Wake_Dipole.m ".
5. The wake coordinates in "WakeL_00.txt" start now at 0. In the previous version the start position was "-5*sigma". Due to this change some of old matlab scripts could have problems.
6. The 1D bunch shape interpolated from particles and indeed used in ECHO is saved in "current0.txt". It is approximately the form factor function.